## Slide 1: Re-tasking Wireless Sensor Networks

## Slide 2: Project Goals
Investigate and analyze Deluge architecture and framework
Design and implement architecture/framework for a selective re-tasking
Design and implement GUI for monitoring and re-tasking network

## Slide 3: History (previous development)
Versioning project with Chris Thames using Deluge (Sensor Networks Fall 2010)
Problems with TinyOS 2.1.1
Very simple approach

## Slide 4: TinyOS Overview
An event driven operating system designed for low-power wireless devices, specifically sensor networks
Language - nesC
Supports many platforms
Open source and actively developed (academia and industry)
Community working groups for documenting and defining new TinyOS standards (TEPs)
Notes: nesC – extension of the C programming language (modules, configurations, interfaces, wiring)

## Slide 5: Iris Mote Overview
Hardware Specs
  Radio Module – 2.4 Ghz IEEE 802.15.4
  ATmega 1281 Microcontroller
    Internal Flash Memory -128K bytes
    8-bit RISC CPU
  Flash Module – 512K Bytes
Operating System
  TinyOS 2.1.2 (August 20, 2012)

## Slide 6: Deluge – Timeline
“An efficient protocol for disseminating large data objects, such as program binaries, to many nodes within a wireless sensor network (Hui 2)”
Timeline
  Paper– Adam Chilipala, Jonathan W. Hui, and Gilman Tolle (Fall 2003, Berkeley)
  Beta Release (April 2004)
  Initial release (Aug 2004)
  Deluge 2.0 Beta (May 2005)
  Deluge 2.0 Release (Jul 2005)
  Current Version Deluge T2 (ported Deluge 2.0 to TinyOS 2.X)
Notes: Hui, Jonathan. Deluge 2.0 – TinyOS Network Programming. July 28, 2005.

## Slide 7: Deluge Overview
nesC reusable component for distributing program binaries
Allows up to four images to be distributed and installed on neighboring motes
Controlled, queried, and commanded using the tos-deluge python script (via serial communication)

## Slide 8: Deluge Mote Configurations
Clients configured with the DelugeC component
Deluge Base station mote
  Compiled as a DELUGE_BASESTATION
  Responsible for forwarding serial messages (received from tos-deluge (python) to the neighboring sensor network (via Dissemination)

## Slide 9: TOS-Deluge
TOS-Deluge (Python Script)
  Injecting and erasing TinyOS applications within the Base station mote (4 slots external flash)
  Initiating the dissemination and reprogram of nodes (network-wide)
Notes: How does a user initiate a reprogram of the network? tos-deluge

## Slide 10: Dissemination
Purpose: Reliably deliver a piece of data to every node (base station to motes)
TEP Standard 118
  Drip implementation
  Trickle timers
The process to push Deluge commands to the motes
  Base station initiates (updates)Deluge command
  Motes receive Deluge command value changed events
Notes: TinyOS Enhancement Proposals (TEP)

## Slide 11: Deluge Overview

## Slide 12: Deluge Architecture
TOSBoot Bootloader
High Level Components:
  Dissemination
  ObjectTransfer
  NetProg
  DelugeManager
  DelugeMetadata
Notes: Bootloader – TOSBOOT
DelugeC

## Slide 13: Deluge Architecture: TOSBoot
Deluge bootloader responsible for the following:
  Reading and writing program binaries between internal and external flash
  Starting the application
  Rollback gesture recognition for loading GoldenImage
Notes: GoldenImage – regarding as a safe/reliable application

## Slide 14: Deluge-TOSBoot Memory Model

## Slide 15: Deluge Architecture: High-Level Components
Notes: Left out all flash/storage components for simplicity

## Slide 16: DelugeC (Top Level)
Listens for Deluge command events (via dissemination)
States
  IDLE
  PUBLISHING
  RECEIVING

## Slide 17: Dissemination Component
Component used to update/receive Deluge commands
  Base station: updates deluge command value
  Clients: receive deluge command changed events

## Slide 18: ObjectTransfer Component
ActiveMessage (AM) based service for sending/receiving program binaries
Each mote runs the ObjectTransfer service
  IDLE
  PUB – service is configured to send image to another mote
  RECV – service is configured to receive image from another mote
Notes: Motes share information – determine who needs an updated image
Images delivered in “Pages”

## Slide 19: DelugeMetadata Component
Reads external flash for information regarding the stored images
  Application Name
  Unique ID
  Timestamp
  Size
  Number of Pages
  CRC (Validity)
Notes: Used to determine if image already exists on mote

## Slide 20: NetProg Component
Module to reprogram and reboot mote (specific to platforms i.e. IRIS)
Writes to internal flash to initiate reprogram (BootArgs)
  Image Address (External Flash)
  TOS_NODE_ID
  DELUGE_GROUP_ID
Forces a hardware reset
Notes: TOSBOOT reads from internal flash and writes the image from external flash to program flash

## Slide 21: DelugeManager Component
Only available to motes that are compiled with the DELUGE_BASESTATION flag
Receives commands (serial) from TOS-deluge (python) and generates Deluge commands for network-wide dissemination

## Slide 22: Current Deluge Limitations
Re-tasking is limited only to network-wide dissemination of program binaries.
Every mote stores and runs the same images
Feedback from the sensor network is limited to the motes’ LEDs

## Slide 23: What did I add to Deluge to achieve the project goals?
Selective re-tasking (preserving current functionality)
Feedback from the sensor network (Collection)

## Slide 24: Selective Re-tasking
Disseminate and reprogram specific motes based on TOS_NODE_ID
Disseminate and reprogram a group of motes based on DELUGE_GROUP_ID
Notes: Backwards compatible

## Slide 25: Re-tasking specific motes
Added node id hash to the Deluge command
Currently node id hash supports up to 32 devices
Each bit represents a node id. If the bit is set then that mote is signaled to be re-tasked
Motes check node id hash before executing command

## Slide 26: Node ID Hash Examples
Node IDs Set | Node ID Hash (32-Bit)
1,2,3,4,5 | 62
29,7,18 | 537133184
10 | 1024
31 | 2147483648

## Slide 27: Re-tasking specific motes example

## Slide 28: Re-tasking group of motes
Added the DELUGE_GROUP_ID preprocessor variable to Deluge
Added groupID variable to the Deluge command
Motes check groupID (originally compiled into image) before executing command
Notes: DELUGE_GROUP_ID set using makefile flag (same process as TOS_NODE_ID)

## Slide 29: Grouping Sensors (via groupID)

## Slide 30: Updating Groups
Added deluge command to update mote groups
Node id hash defines the motes to update and groupID specifies the new group

## Slide 31: Update Group with new Motes

## Slide 32: Deluge High-Level Components with Collection

## Slide 33: Deluge Collection
Purpose: Gather information about the sensor network (motes to base station)
TEP Standard 119
  Based on trees using a link estimator algorithm for building efficient/reliable routes between nodes and base station
  Best-effort, multihop delivery of packets to the root of a tree
Notes: TinyOS Enhancement Proposals (TEP)
Reverse of dissemination

## Slide 34: Collection Message: NodeStatus
Fields
  Node ID
  Group ID
  State
  Current Running Application
    Unique ID
    Name
    Time Stamp
Limited to 20 bytes per payload
Notes: 20 byte limit for collection payloads (took a while to figure this out)

## Slide 35: Deluge Overview with Monitoring

## Slide 36: Deluge Code Size
Application | ROM (Bytes) | RAM (Bytes) | ROM Δ | RAM Δ
Blink (Deluge) | 26666 | 957 | +2.3% | +1.3%
Base station (Deluge) | 32840 | 1315 | +1.0% | +1.2%
Application | ROM (Bytes) | RAM (Bytes)
Blink (Deluge) | 26074 | 945
Base station (Deluge) | 32544 | 1300
Application | ROM (Bytes) | RAM (Bytes) | ROM Δ | RAM Δ
Blink (Deluge) | 33294 | 2127 | + 28% | 125%
Base station (Deluge) | 39614 | 2463 | + 22% | 89%
Original Deluge (2.1.2)
Deluge w/o Collection (Monitoring)
Deluge with Collection (Monitoring)

## Slide 37: Deluge Visualizer
Purpose:
  TOS-Deluge Frontend for issuing commands
  Status window for displaying tos-deluge output
  Dynamic table displaying information and state about the sensor devices
Cross platform: JAVA
Built using the TinyOS JAVA SDK and MIG tool
Notes: MIG - used to auto-generate language specific serialization code
TinyOS SDK also includes C, C++, JAVA, and PYTHON

## Slide 38: Deluge Visualizer Components

## Slide 39: Deluge Visualizer Application
Notes: 3 sections – dynamic node status table, tos-deluge gui frontend, and status window

## Slide 40: Development Tools/Process
Source Control: Mercurial
Wiki: Chiliproject
Ubuntu 12.04
Windows 7 running Ubuntu 12.04 VM (via VirtualBox)

## Slide 41: IRIS Mote Debugging
PrintF
TOSSIM (python jig)
LEDS

## Slide 42: Conclusion
Successfully completed project goals
  Maintained current network-wide re-tasking features
  Implemented selective re-tasking
  Implemented monitoring framework and application

## Slide 43: Future Work
Improve memory (ROM/RAM) footprint
Remove dependency on tos-deluge
Add support for Android TinyOS SDK

## Slide 44: References
TinyOS Wiki: http://docs.tinyos.net/tinywiki/index.php/Main_Page
TEPs: http://docs.tinyos.net/tinywiki/index.php/TEPs
Deluge Documentation: http://www.cs.berkeley.edu/~jwhui/deluge/documentation.html
Notes: TinyOS Enhancement Proposals (TEP

## Slide 45: Live Demonstration